## Slide 1: 1.Create a network diagram showing:
Router
Switch
Firewall
At least 3 client devices
Internet connection
Wireless access point

## Slide 2: Diagram
☁️ INTERNET
|
🔥 FIREWALL
|
📡 ROUTER
/ \
/ \
🔌 SWITCH 📶 ACCESS POINT
/ | \ |
/ | \ |
💻 PC 🖨️ Printer 💻 Laptop 📱 Phone

## Slide 3
Quick Understanding
☁Internet → The outside world
🔥 Firewall → Security guard protecting the network
📡 Router → Directs internet traffic
🔌 Switch → Connects wired devices
📶 Access Point → Provides Wi-Fi
💻📱🖨️ Clients → Devices people use

## Slide 4
📱 Phone
↓
📶 Access Point (Wi-Fi)
↓
📡 Router
↓
🔥 Firewall
↓
☁️ Internet

## Slide 5: 2.Match the following technologies to their correct OSI layer:
HTTP
HTTPS
TCP
UDP
IP
ARP
DNS
SMTP

## Slide 6
Technology | OSI Layer | Function
HTTP | Application Layer (Layer 7) | Used for web browsing
HTTPS | Application Layer (Layer 7) | Secure web browsing
TCP | Transport Layer (Layer 4) | Reliable data delivery
UDP | Transport Layer (Layer 4) | Fast but less reliable delivery
IP | Network Layer (Layer 3) | Handles addressing and routing
ARP | Data Link Layer (Layer 2) | Finds MAC addresses from IP addresses
DNS | Application Layer (Layer 7) | Translates domain names to IP addresses
SMTP | Application Layer (Layer 7) | Sends emails

## Slide 7: Simple Way To Understand It
Think of the OSI model like delivering a package in Enugu.
Application Layer → Where users interact (Browser, email, websites)
Transport Layer → Ensures delivery (Like a delivery company checking parcels)
Network Layer → Finds the destination (Road directions and addresses)
Data Link Layer → Connects devices locally (House-to-house connection inside the same street)

## Slide 8
HTTP, HTTPS, DNS, SMTP → Users and applications
TCP, UDP → Delivery methods
IP → Addressing and routing
ARP → Finds device hardware address (MAC)

## Slide 9: 3.Create a table containing:
Protocol name
Purpose
TCP/UDP
Port number
Security purpose
for the various technologies below
HTTP
HTTPS
DNS
DHCP
ARP
ICMP
SSH
SMTP
IMAP
POP3

## Slide 10
Protocol | Purpose | TCP/UDP | Port | Security Purpose
HTTP | Web browsing | TCP | 80 | Basic communication
HTTPS | Secure web browsing | TCP | 443 | Encrypts data
DNS | Name to IP translation | UDP/TCP | 53 | Finds correct servers
DHCP | Assigns IP addresses | UDP | 67/68 | Reduces configuration errors
ARP | Finds MAC address | Neither | N/A | Local device identification

## Slide 11
Protocol | Purpose | TCP/UDP | Port | Security Purpose
ICMP | Network testing | Neither | N/A | Troubleshooting
SSH | Secure remote login | TCP | 22 | Encrypted access
SMTP | Sends emails | TCP | 25 | Secure mail transfer
IMAP | Access emails on server | TCP | 143 | Secure synchronization
POP3 | Downloads emails | TCP | 110 | Secure email retrieval

## Slide 12: Simple Understanding
Think of these protocols like workers inside a company in Enugu:
HTTP/HTTPS → Website delivery workers
DNS → Phonebook directory
DHCP → Office admin assigning addresses
ARP → Person finding exact house location
ICMP → Inspector testing the network
SSH → Secure office entrance
SMTP/IMAP/POP3 → Post office handling emails

## Slide 13: To understand it more
HTTPS & SSH = Secure communication
DNS & DHCP = Network setup helpers
SMTP, IMAP, POP3 = Email protocols
ICMP = Troubleshooting
ARP = Device identification inside local network

## Slide 14: 4.Identify which protocols are secure and insecure and explain why organizations should avoid insecure protocols.
HTTP vs HTTPS
Telnet vs SSH
Encryption

## Slide 15
Protocol | Type | Security Level | Why
HTTP | Insecure | ❌ Not safe | Data is sent in plain text (can be intercepted)
HTTPS | Secure | ✅ Safe | Data is encrypted using SSL/TLS
Telnet | Insecure | ❌ Not safe | Sends login details in plain text
SSH | Secure | ✅ Safe | Encrypts all remote login communication

## Slide 16: Simple Explanation
HTTP = shouting your message in the open market at Enugu 👉 Anyone nearby can hear it
HTTPS = whispering inside a locked room 👉 Only the intended website understands it
Telnet = entering a building with no gate or security 👉 Anyone can see your password
SSH = entering with fingerprint + locked door 👉 Everything is hidden and protected

## Slide 17: What is Encryption?
Encryption is the foundation of security.
👉 It means converting readable data into unreadable code.
Example:
Normal message: “Send ₦5000”
Encrypted message: “X9#kL2@pQ!”
Only the receiver with the correct “key” can decode it.

## Slide 18: 5A Create a comparison table for IPv4 , IPv6 showing:
Address format
Length
Example
Advantages
Limitations

## Slide 19
Feature | IPv4 | IPv6
Address Format | Numeric dotted decimal | Hexadecimal separated by colons
Length | 32-bit | 128-bit
Example | 192.168.1.1 | 2001:0db8:85a3::8a2e:0370:7334
Advantages | Simple, widely used, compatible with most systems | Huge address space, faster routing, better security
Limitations | Limited addresses, NAT required, running out of IPs | More complex, not fully supported in older systems

## Slide 20: Simple Understanding
Think of IP addresses like house numbers in Enugu:
🏠 IPv4
Like old Enugu streets with limited house numbers
Eventually, houses run out of numbers
People start sharing addresses (NAT problem)
🏙️ IPv6
Like a modern city expansion plan
Unlimited house numbering system
Every device gets its own unique address
In essence
IPv4 = “Old system, limited space”
IPv6 = “Modern upgrade, massive expansion”

## Slide 21: 5B.Identify the following;
your private IP address.
your public IP address and
Explain the role of NAT.

## Slide 22: 1. Your Private IP Address
A private IP address is the address your device gets inside your local network (home Wi-Fi, office network, hotspot).
📌 Example formats:
192.168.x.x
10.x.x.x
172.16.x.x – 172.31.x.x
Meaning:
It is only visible inside your network, not on the internet.

## Slide 23: 2. Your Public IP Address
A public IP address is the address given to your router by your Internet Service Provider.
📌 Example:
102.89.45.12
197.210.123.44
Meaning:
This is what the entire internet sees you as.
👉 So if you open Google in Enugu, Google does NOT see your phone IP It sees your public IP from MTN/Airtel/Spectranet/etc.

## Slide 24: 3. Role of NAT (Network Address Translation)
NAT is the bridge between private and public IPs.
Simple Definition:
NAT is the system in your router that converts many private IP addresses into one public IP address for internet access.

## Slide 25: 🔄 How NAT Works
📱 Phone (192.168.1.5)
💻 Laptop (192.168.1.6)
🖥️ PC (192.168.1.7)
↓
📡 ROUTER (NAT)
↓
🌍 Internet uses ONE public IP

## Slide 26: Real-Life Analogy
Think of a compound in Abakpa:
Every tenant has a room number (private IP)
But the outside world only sees the compound address (public IP)
👉 The compound gatekeeper (router + NAT):
Receives all messages
Sends them out using one official address
Brings replies back to the correct person

## Slide 27: 6.Identify the subnet mask for a given CIDR notation
Determine:
Network address
Broadcast address
Available hosts

## Slide 28: Subnetting (CIDR → Network Details)
To solve this properly, I need a CIDR example. Since you didn’t specify one, 👉 Example CIDR: 192.168.10.0/24

## Slide 29: What is CIDR and Subnetting?
What is CIDR and Subnetting?
Subnetting is simply:
Dividing a network into smaller manageable parts.
CIDR notation looks like this: 192.168.10.0/24
The /24 is the important part.
It tells us:
How much belongs to the network
How much belongs to the devices (hosts)

## Slide 30
Part | Meaning
192 | Fixed
168 | Fixed
10 | Fixed
0-255 | Device area
Find the Subnet Mask
/24 means:
255.255.255.0
Why?
Because:
255 means “locked/fixed”
0 means “available for devices”
So:

## Slide 31: Find the Network Address
The network address is: 👉 the FIRST address in the range.
For this network:
192.168.10.0
This identifies the network itself.
⚠️ You cannot give this to a device.
Think of it like; “Ogui Road” itself, not a particular house.

## Slide 32: Find the Broadcast Address
The broadcast address is: 👉 the LAST address in the range.
For /24:
192.168.10.255
This sends messages to ALL devices.
Think of it like: 📢 A town crier shouting to the entire street.

## Slide 33: Find Available Hosts
The last number ranges from:
0 → 255
That gives:
256 total addresses
BUT:
1 is reserved for Network Address
1 is reserved for Broadcast Address
So:
256 - 2 = 254 usable hosts

## Slide 34: Breakdown
Item | Meaning | Value
CIDR | Network size | /24
Subnet Mask | Defines network boundary | 255.255.255.0
Network Address | First address | 192.168.10.0
Broadcast Address | Last address | 192.168.10.255
Usable Hosts | Devices allowed | 254

## Slide 35: Another way to understand it
192.168.10.0 → Network Address
192.168.10.1
192.168.10.2
192.168.10.3
...
192.168.10.254 → Last usable host
192.168.10.255 → Broadcast Address

## Slide 36: 7. Create a comparison table for:
Hardware firewall
Software firewall
Cloud firewall
Stateful firewall
Stateless firewall
NGFW

## Slide 37
Firewall Type | Description | Advantages | Limitations | Common Use
Hardware Firewall | Physical device placed between network and internet | Strong protection for entire network | Expensive | Companies and offices
Software Firewall | Installed on a computer or server | Easy to install and manage | Protects only one device | Personal computers
Cloud Firewall | Firewall hosted on the internet/cloud | Scalable and remote access protection | Depends on internet/cloud provider | Cloud applications and remote work
Stateful Firewall | Tracks active connections before allowing traffic | Better security and traffic monitoring | Uses more resources | Enterprise networks
Stateless Firewall | Checks packets individually without tracking sessions | Faster performance | Less secure | Simple or older networks
NGFW (Next-Generation Firewall) | Advanced firewall with deep inspection and threat detection | Detects malware, attacks, and applications | Costly and complex | Modern enterprise security

## Slide 38
Easy way to understand
Hardware = Physical protection
Software = Device protection
Cloud = Online protection
Stateful = Remembers connections
Stateless = Checks packets only
NGFW = Advanced intelligent firewall .
In Essence
A firewall controls incoming and outgoing traffic to protect systems from unauthorized access and cyber threats. Different firewall types provide different levels of security, speed, and management depending on organizational needs.

## Slide 39: 8. Create a report explaining:
Purpose of VPN
Remote access VPN
Site-to-site VPN
IPSec
Wire Guard
VPN encryption

## Slide 40: VPN Report
A VPN (Virtual Private Network) is a secure connection that allows users or organizations to send data safely over the internet.
It creates an encrypted “private tunnel” between devices and networks so outsiders cannot easily see or steal the information.
Think of it like traveling through a hidden underground tunnel instead of using an open public road.

## Slide 41
Purpose of VPN
The main purpose of a VPN is to:
Protect sensitive information
Secure internet communication
Allow safe remote access
Hide user activity from attackers
Connect networks across different locations
Organizations use VPNs to protect:
Employee communications
Company files
Financial transactions
Internal systems

## Slide 42
🏠 Remote Access VPN
A Remote Access VPN allows an individual user to securely connect to a company network from another location.
How It Works
User connects to internet
VPN creates encrypted tunnel
User securely accesses company network
Advantages
Secure remote work
Protects data on public Wi-Fi
Allows access from anywhere

## Slide 43
🏢 Site-to-Site VPN
A Site-to-Site VPN securely connects two different office networks over the internet.
Example
A company branch in Enugu connects securely to headquarters in Abuja.
Employees in both offices can share:
Files
Servers
Printers
Applications
as if they are in the same building.
Advantages
Secure branch communication
Reduces networking costs
Centralized access

## Slide 44
🔐 IPSec (Internet Protocol Security)
IPSec is a VPN security protocol used to encrypt and protect IP communication.
It works mainly at the:
Network Layer (Layer 3)
Functions of IPSec
Encrypts data
Authenticates users
Protects against tampering
Common Use
Widely used in:
Enterprise VPNs
Site-to-site VPNs
⚠️ Limitation
Can be complex to configure.

## Slide 45
⚡ WireGuard
WireGuard is a modern VPN protocol designed to be:
Faster
Simpler
More secure
than older VPN technologies.
Advantages
High speed
Lightweight
Strong encryption
Easier configuration
Common Use
Used in:
Modern VPN services
Mobile devices
Cloud environments

## Slide 46
🔒 VPN Encryption
VPN encryption converts readable data into unreadable code during transmission.
Simple Meaning
Even if hackers intercept the traffic: They cannot understand the information.
Example
Normal message:
Password123
Encrypted message:
X#4!pL9@Qz
Only authorized users with the correct encryption key can decode it.

## Slide 47: Conclusion
VPNs are essential cybersecurity tools that secure communication across public networks. Technologies such as Remote Access VPN, Site-to-Site VPN, IPSec, and Wire Guard help organizations protect sensitive information, support remote work, and maintain secure communication between locations through strong encryption mechanisms.

## Slide 48: 9.Create a comparison table containing:
Encryption strength
Security weaknesses
Recommended usage
Security improvements
for the below technologies
WEP
WPA
WPA2
WPA3

## Slide 49
Technology | Encryption Strength | Security Weaknesses | Recommended Usage | Security Improvements
WEP | Weak | Easily cracked by attackers | ❌ Not recommended | First wireless security standard
WPA | Moderate | Vulnerable to some attacks | ⚠️ Temporary/legacy use only | Improved encryption over WEP
WPA2 | Strong | Can still face password brute-force attacks | ✅ Widely recommended | Uses AES encryption for stronger security
WPA3 | Very Strong | Limited support on older devices | ✅ Best modern choice | Stronger authentication and better encryption

## Slide 50: Real life analogy
Technology | Real-Life Analogy
WEP | Old weak padlock
WPA | Better lock but still vulnerable
WPA2 | Strong modern security door
WPA3 | Smart biometric security system

## Slide 51
Quick Breakdown
❌ WEP
Very old wireless security
Hackers can break it quickly
Should never be used today
⚠️ WPA
Better than WEP
Introduced stronger protection
Still outdated now
✅ WPA2
Most common modern Wi-Fi security
Uses strong AES encryption
Good for homes and businesses
🔥 WPA3
Latest and strongest Wi-Fi protection
Better password security
Safer against brute-force attacks

## Slide 52: 10.Create a diagram showing:
Internet
Firewall
DMZ
Internal network
Restricted zone

## Slide 53
      ☁️ INTERNET
|
|
🔥 FIREWALL
/ | \
/ | \
/ | \
🌐 DMZ 🏢 INTERNAL 🔒 RESTRICTED ZONE
(Public Zone) NETWORK |
| |
💻 Office PCs 🗄️ Sensitive Servers
🖨️ Printers 💰 Financial Data

## Slide 54
              Simple Understanding
☁️ Internet
The outside world where users and attackers exist.
🔥 Firewall
The security guard controlling who enters and leaves the network.
🌐 DMZ (Demilitarized Zone)
A semi-public area for services people outside can access safely.
Examples: Web servers, Email servers, or Company websites.
👉 If attackers compromise the DMZ, the internal network is still protected.

## Slide 55
🏢 Internal Network
The main company network where staff work.
Contains: Employee computers, Printers, or Internal systems.
🔒 Restricted Zone
The highest security area.
Contains: Financial databases, Sensitive records, or Critical servers.
Only authorized users can enter.

## Slide 56
Real life Analogy
Think of a big company estate in Enugu:
Network Area | Real-Life Example
Internet | Outside public road
Firewall | Estate security gate
DMZ | Reception area for visitors
Internal Network | Main office building
Restricted Zone | Locked executive vault room

## Slide 57
11.Create a report describing:
How each attack works
Possible impact
Security risks
Basic prevention methods
Attacks:
Packet sniffing
IP spoofing
DoS
DDoS
Backdoor attack
On-path attack

## Slide 58
    Cybersecurity Attack Report
Cyberattacks are methods used by attackers to steal information, interrupt services, or gain unauthorized access to systems and networks. Organizations use cybersecurity controls to reduce these threats and protect sensitive information.

## Slide 59
1. 📦 Packet Sniffing
How It Works
Packet sniffing involves capturing and monitoring network traffic moving across a network.
Attackers use tools to read: Passwords, Emails, or Sensitive data.
especially when information is not encrypted.
Possible Impact
Data theft
Password exposure
Privacy violations
Security Risks
Unencrypted communication can easily be intercepted.
Prevention Methods
Use HTTPS and VPNs
Encrypt network traffic
Avoid public unsecured Wi-Fi

## Slide 60
2. 🎭 IP Spoofing
How It Works
The attacker changes their IP address to appear as a trusted device or user.
This helps attackers: Bypass security controls, and Hide their identity.
Possible Impact
Unauthorized access
Data manipulation
Network attacks
Security Risks
Systems may trust fake devices or users.
Prevention Methods
Use firewalls
Enable packet filtering
Use authentication systems

## Slide 61
3. 🚫 DoS (Denial of Service)
How It Works
A DoS attack floods a server or network with excessive traffic until it becomes unavailable.
Possible Impact
Website downtime
Service interruption
Loss of productivity
Security Risks
Legitimate users cannot access services.
Prevention Methods
Traffic filtering
Firewalls
Rate limiting

## Slide 62
4. 🌍 DDoS (Distributed Denial of Service)
How It Works
Similar to DoS, but traffic comes from many infected computers (botnets) at the same time.
Possible Impact
Large-scale outages
Financial losses
Reputation damage
Security Risks
Very difficult to stop because attacks come from multiple locations.
Prevention Methods
DDoS protection services
Load balancing
Network monitoring

## Slide 63
5. 🚪 Backdoor Attack
How It Works
Attackers secretly install hidden access methods into systems or software.
This allows them to enter later without authorization.
Possible Impact
Remote control of systems
Data theft
Malware installation
Security Risks
Attackers maintain hidden long-term access.
Prevention Methods
Regular software updates
Antivirus and endpoint security
Access monitoring

## Slide 64
6. 🛣️ On-Path Attack (Man-in-the-Middle)
How It Works
The attacker secretly intercepts communication between two parties.
The attacker can:
Read messages
Modify data
Steal credentials
without either side noticing.
Possible Impact: Financial fraud, Stolen passwords, and Data manipulation.
Security Risks
Sensitive communication becomes compromised.
Prevention Methods: Use HTTPS, Use VPNs, or Enable encryption and authentication.

## Slide 65: Real-Life Analogy Imagine sending confidential business documents across Enugu:
Attack | Real-Life Analogy
Packet Sniffing | Somebody secretly reading your letters
IP Spoofing | Criminal pretending to be a trusted worker
DoS | Blocking a shop entrance so customers cannot enter
DDoS | Hundreds of people blocking the entrance at once
Backdoor Attack | Secret hidden entrance into a building
On-Path Attack | Intercepting and altering messages between two people

## Slide 66: In conclusion
Cyberattacks threaten confidentiality, integrity, and availability of information systems. Organizations reduce these risks by implementing strong security practices such as encryption, firewalls, authentication, software updates, monitoring, and secure communication technologies.

## Slide 67: 12. Create a security hardening checklist for:
Personal computer
School network
Company workstation

## Slide 68
🔐 Security Hardening Checklist
Security hardening means strengthening systems to reduce vulnerabilities and protect against cyberattacks.

## Slide 69: 💻 1. Personal Computer Security Checklist
Security Measure | Purpose
Install antivirus software | Detects and blocks malware
Enable firewall | Controls unauthorized access
Use strong passwords | Prevents unauthorized login
Enable automatic updates | Fixes security vulnerabilities
Use multi-factor authentication (MFA) | Adds extra login protection
Avoid suspicious downloads | Prevents malware infection
Backup important files | Protects against data loss
Use encrypted Wi-Fi (WPA2/WPA3) | Secures wireless communication

## Slide 70: 🏫 2. School Network Security Checklist
Security Measure | Purpose
Deploy network firewall | Protects school network traffic
Separate student and staff networks | Reduces unauthorized access
Use content filtering | Blocks harmful websites
Enable user authentication | Controls network access
Monitor network activity | Detects suspicious behavior
Secure Wi-Fi with WPA2/WPA3 | Prevents unauthorized connections
Regularly update systems | Fixes vulnerabilities
Restrict USB device usage | Prevents malware spread

## Slide 71: 🏢 3. Company Workstation Security Checklist
Security Measure | Purpose
Use endpoint protection software | Detects advanced threats
Enforce strong password policy | Improves account security
Enable disk encryption | Protects sensitive company data
Apply least privilege access | Limits unnecessary permissions
Lock workstation when idle | Prevents unauthorized use
Use VPN for remote access | Secures remote communication
Disable unused ports/services | Reduces attack surface
Conduct regular security training | Improves employee awareness

## Slide 72: Simple Analogy Think of cybersecurity like protecting buildings in Enugu:
Security Action | Real-Life Meaning
Firewall | Security gate
Antivirus | Security patrol
Passwords | Door locks
MFA | Extra gate verification
Encryption | Locked safe
Updates | Repairing weak doors/windows

## Slide 73: Final Summary
Security hardening reduces risks by applying protective controls such as firewalls, encryption, updates, authentication, monitoring, and user awareness. Proper hardening improves confidentiality, integrity, and availability of systems and networks.